## Slide 1: MEBT Quadrupoles
Scott Lawrie
FETS Meeting
UCL, 8th May 2013

## Slide 2: Quadrupole Specifications
Pole-tip inscribed radius = 21.5 mm
  41.5 mm OD vacuum pipe
  1 mm for alignment, 0.5 mm contingency
B-field gradient = 18 Tm-1
Max. total length inc. coils = 70 mm
3380 A.Turns per pole
Individually powered + dipole windings

## Slide 3: Dipole Winding Specs
Each quad has x & y embedded steerers
Extra winding, not separated quad coils
Maximum deflection angle given by:
For 3 MeV H–, need an integrated field of:
Opera suggests need 360 A.Turns for this

## Slide 4: Difficulties with Specs
Bore > 1/2 total length
  Fringe fields very important (2D insufficient)
  Difficult to ensure good field quality
70 mm total length includes coils
  Very little space for coils: Need few # turns
Individually powered + dipole windings
  Possibly £££ on power supplies alone
  Power ∝ Current Density
  Allow space for dipole windings

## Slide 5: Power Supplies
TDK-Lambda Genesys 6-200
200 A, 6 V  1200 W in 1U chassis
Same family as used on ISIS linac quads
£1,405 base price + multi-buy discount
 18 turns of (5x5)mm2 hollow conductor

## Slide 6: High Gradient  Straight Poles
Straight poles saturate badly at high gradients, reducing homogeneity and increasing magnetic length

## Slide 7: Tapered Pole

## Slide 8: 3D Tapered Pole Not Saturating
Note: Coils shown are simple racetracks. Give same results as realistic tapered coils but much faster to solve!

## Slide 9: Magnetic Length
Final design has integrated field

## Slide 10: Higher Order Harmonics

## Slide 11: Integrated Field Homogeneity

## Slide 12: Linearity with Applied Current

## Slide 13: Quad & Dipole Coils Energised

## Slide 14: Mechanical Considerations
Machine from solid steel (not laminations)
How to bolt together (Re: dipole windings)
Datums/mounting
Placement of connections/manifold
Thorough quotation request document
   Danfysik, SigmaPhi, Scanditronix, Tesla

## Slide 15: Summary
Each magnet fits within 70 mm space
18 Turns, up to 200 A (water cooled)
Up to 19.2 Tm-1 quad, 12 mT dipole
72.7 mm magnetic length
Nice linear performance
Reasonable homogeneity & harmonics
1200 W power supplies sourced
Aim for quotes ready by June