## Slide 1: Progress on the VESPA: The Road to a 100 mA Beam
FETS Meeting
13th February 2013

## Slide 2: Vessel for Extraction and Source Plasma Analyses: VESPA
Purpose-built test stand to study and improve ISIS/FETS ion source
  Plasma
  Beam Transport
  Reliability/Longevity
Plasma and beam diagnostics
More efficient beam extraction optics

## Slide 3
Two versions with different aims:
VESPA Mk 1
  Proof of principle: not optimal design
  Re-use existing vessel and parts: cost-effective
  Operating at present
VESPA Mk 2
  Built for purpose: optimised layout
  Multiple diagnostics
  Compatible with ISIS upgrade schemes
  In design at present

## Slide 4: VESPA Mk 1
Vacuum Pump
Platform Ground
+
-20 kV DC Platform Power
Vacuum Window
–
Laboratory Ground
Protection & ‘Scope
Faraday Cup Within Shield
+16 kV Pulsed Extract Power
+
–
Ion Source
-20 kV
-4 kV
0 kV
B-Field

## Slide 5: VESPA Mk 1 Internals

## Slide 6: VESPA Mk 2
2000 L/s Vacuum Pump
Emittance Scanners
Optical Monochromator
Retractable Faraday Cup
Post-acceleration Electrodes
View-ports
35 kV Insulator
‘Top-loading’ Ion Source
Vacuum Gauges
+
–
+20 kV Pulsed Extract Power
-35 kV DC Platform Power
+
–
Vacuum Window

## Slide 7: VESPA Mk 2 Present CAD Design

## Slide 8: VESPA Mk 1 Results
100 mA of H–!
35 A arc
13 kV extract
45 A arc
15 kV extract
55 A arc
16 kV extract

## Slide 9: “What About the Electrons?”
H– beam deflected by B-field
e– suppressed by E & B-fields
100 mA extracted H–
1000 mA extracted e–
93.5 mA H– to Faraday cup
2.4 mA e– to Faraday cup
Model Geometry
Equipotentials
Extracted H–
Extracted e–
Background e–
Secondary e–
-8 kV
0 kV
+8 kV

## Slide 10: To do…
Sort out sparking problem
Make definitely sure no e– measured
  Extractor negative relative to lab ground
  Dedicated magnetic deflector?
Confirm design of (and build) VESPA Mk 2
Design better extraction system
Clear out lab space